## Slide 1
Partition into Hybrid Processor/Accelerator System
Hybrid Design Flow
Partition is based on benefits of acceleration
Compilation
Execution & Profiling
Partition Analysis
LegUp HLS
Hybrid System
Notes: 1

## Slide 2
Hybrid System Cycle Prediction
Slow to profile a hybrid system
  Synthesize to FPGA programming bit-stream
  Simulate the system via ModelSim
Goal
  Quick/early prediction of the speed benefits of accelerating a function in HW
Gain = SW cycle / Hybrid Cycle
  SW cycle: HW profiler
  Hybrid cycle: Prediction
Notes: 2

## Slide 3
Hybrid System Execution Flow
4 Components:
SW wrapper
  fetch instruction
  store arguments
  trigger start signal
FSM in accelerator
Data loads
Data stores
Accelerator
Instr. Cache
SDRAM
BB_0:
s0: reg <= data;
s1: ****
BB_1:
s2: ****
s3: ****
s4: ****
BB_2:
s5: load from global memory
s6: store to global memory
µP
000: addi a0, 0, a0
004: jal 0x100 //call wrapper
…
100: sw a0, 0(v1) //store argument
104: sw a1, 0(v0) //start accelerator
108: jr ra //return
Data Cache
assert stall_cpu
write arguments
start
release stall_cpu
Notes: 3

## Slide 4
Instruction Fetch
  (# of hits) + 13*(# of misses)
Argument Overhead
  ~2 cycles to store each argument
  2*(# of arguments)*(# of runs)
SW/HW Transition
  Constantly 2 cycle to transit b/w HW & SW
  2*(# of runs)
Component I - SW Wrapper
MIPS Emulator
Substitute Wrapper
Cache Simulator
Pure SW Program Binary
Instr. Trace in
Pure SW System
Estimated Instr. Trace in
Hybrid System
Instr. $:
# of hits
# of misses
Notes: 4

## Slide 5
Component I - SW Wrapper
Contribution to Total Tolerance
  (actual cycle – estimated cycle) / actual hybrid cycle
  Average: 3.01%
  StdDev: 4.04%
Note: Total Tolerance =
  (actual hybrid cycle – predicted hybrid cycle) / actual hybrid cycle
Chart: Error Distribution of SW Wrapper Cycle
| <5% | 5%~10% | 10%~15% | 15%~20% | 20%~25% | 25%~30% | 30%~35% | >35%
SW Wrapper Cycle Tolerance | 35 | 9 | 2 | 1 | 0 | 0 | 0 | 0
Notes: 5

## Slide 6
Component II – HW Cycle
Sched. Length in Cycle of each BB
# of times each BB runs
Schedule the Accel. Function
Execute Program in SW
Combine
# of BB runs w/ sched. lengthes
Estimated. HW cycle of accelerator
∑ foreach BB (sched. length) * (# of runs)
Accurate if no mem. access
Contribution to Total Tolerance
  Average: 0.02%
  StdDev: 0.16%
Note: 1 of 47 tests contributes 1.09% tolerance; all other 46 tests: 0%
LegUp
IR interpreter
Notes: 6

## Slide 7
Component III – Data Loads
MIPS Emulator
Address Filter
Global CONST
Local Stack
Cache Simulator
Pure SW Program Binary
Load Trace:
load A1
load A2
load A3
load A4
load A5
...
…
Data $:
# of hits
# of misses
Load Trace:
load A1
load A3
load A5
...
…
  Cycles to load data:
  (# of hits) + 31*(# of misses)
Notes: 7

## Slide 8
Component III – Data Loads
Contribution to Total Tolerance
  Average: 0.97%
  StdDev: 1.73%
Chart: Error Distribution of Data Load Cycle
| <5% | 5%~10% | 10%~15% | 15%~20% | 20%~25% | 25%~30% | 30%~35% | >35%
Data Cache Cycle Tolerance | 45 | 2 | 0 | 0 | 0 | 0 | 0 | 0
Notes: 8

## Slide 9
Component IV – Data Stores
Similar Methodology as Data Loads
  Generate address trace in the same way as Data Loads
  Write-through policy of data cache
  1.85*(# of stores)
Contribution to Total Tolerance
  Average: 5.35%
  StdDev: 7.86%
  Most Inaccurate – “Key Contributer” to total tolerance
Chart: Error Distribution of Data Store Cycle
| <5% | 5%~10% | 10%~15% | 15%~20% | 20%~25% | 25%~30% | 30%~35% | >35%
Data Store Cycle Tolerance | 34 | 4 | 4 | 3 | 0 | 0 | 2 | 0
Notes: 9

## Slide 10
Final Result – Predicted Hybrid Cycle
Sum of
  SW Wrapper Cycle
  HW Cycle
  Data Load Cycle
  Data Store Cycle
Average: 7.21%
StdDev: 7.79%
Chart: Error Distribution of Predicted Hybrid Cycle
| <5% | 5%~10% | 10%~15% | 15%~20% | 20%~25% | 25%~30% | 30%~35% | >35%
Hybrid Cycle Tolerance | 25 | 9 | 8 | 3 | 0 | 0 | 2 | 0
Notes: 10

## Slide 11
“Key Contributor” to Tolerance
– Data Store Cycle
The only 2 tests that have tolerance greater 20%
Data Store Cycle = 1.85 * (# of stores)
 | Function A | Function B
Hybrid Cycle Tolerance | 32.26% | 34.39%
Tolerance Contributed by Data Store Cycle | 32.32% | 31.56%
Estimated # of Stores | 4000 | 18432
Actual # of Stores | 4100 | 18624
Estimated Store Cycles | 7400 | 34099
Actual Store Cycles | 22445 | 110524
Varying Coefficient | 5.47 | 5.93
Open-Row architecture in the SDRAM on DE-II
  ~1 cycle to store data in currently open row
  A lot more cycles to store data in a different row
Chart: Hybrid Cycle Tolerance vs. Data Store Cycle Tolerance
| adpcm_main | decode | encode | filtez | quantl | upzero | AddRoundKey_InversMixColumn | aes_main | ByteSub_ShiftRow | decrypt | encrypt | InversShiftRow_ByteSub | KeySchedule | MixColumn_AddRoundKey | BF_cfb64_encrypt | BF_encrypt | BF_set_key | blowfish_main | float64_add | propagateFloat64NaN | roundAndPackFloat64 | shift64RightJamming | float64_div | float64_mul | mul64To128 | propagateFloat64NaN | float64_add | float64_div | sin | Autocorrelation | Gsm_LPC_Analysis | gsm_mult_r | Reflection_coefficients | buf_getb | buf_getv | ChenIDct | YuvToRgb | Fill_Buffer | Flush_Buffer | Initialize_Buffer | motion_vector | motion_vectors | read | memcpy | sha_stream | sha_transform | sha_update
Hybrid Cycle Tolerance | 0.14747 | 0.32258 | 0.13928 | 0.026667 | 0.0069832 | 0.021585 | 0.0010285 | 0.10187 | 0.080948 | 0.036409 | 0.049748 | 0.098919 | 0.14814 | 0.11776 | 0.007889 | 0.020005 | 0.014962 | 0.0055227 | 0.073838 | 0.11278 | 0.014417 | 0.016423 | 0.030565 | 0.092077 | 0.029018 | 0.089474 | 0.055113 | 0.013445 | 0.0058072 | 0.091058 | 0.074996 | 0.048079 | 0.0097087 | 0.1037 | 0.079894 | 0.0040345 | 0.34395 | 0.19048 | 0.1804 | 0.18932 | 0.0015385 | 0.10486 | 0.028669 | 0.036109 | 0.012171 | 0.00074538 | 0.0059148
Data Store Cycle Tolerance | 0.14809 | 0.32316 | 0.13722 | 0 | 0 | 0.026804 | 0.0014025 | 0.09629 | 0.056419 | 0.026716 | 0.036916 | 0.07315 | 0.13405 | 0.015195 | 0.02921 | 0.0031583 | 0.014164 | 0.0051075 | 0.00091158 | 0 | 0 | 0.072993 | 0.0019934 | 0.0021413 | 0.11384 | 0 | 0.0088279 | 0.003597 | 0.0084596 | 0.049073 | 0.042855 | 0 | 0.0084951 | 0.0038568 | 0.014819 | 0.031786 | 0.31555 | 0.18988 | 0.18374 | 0.19025 | 0.027692 | 0.015135 | 0.044331 | 0.034188 | 0.011952 | 0.0015045 | 0.010168
Most of the tolerances come from data store cycle estimation
Notes: 11

## Slide 12
THANK YOU !